Electric Motor Lab

Name: __________________				Date: __________________

The purpose of today’s activity is for you to build a simple electric motor and to use your understanding of electricity and magnetism to understand what is happening. Your product for this lab will be the answers to the questions written out neatly, with your coil attached to the paper. Complete one of the options at the end to go above and beyond. Please choose an option that you are interested in and that you find challenging.

Materials needed:

- 1 meter of insulated wire

- 2 paper clips

- clay

- batteries

- lab bar to wrap wire around

- sandpaper

- magnet

- Wrap the wire around the lab bar leaving about 3 cm of wire on each end.

- Slide the wire off the lab bar, holding on to the coil so that it does not come apart. Wrap the ends of the coil around the coils so that it stays together. You should get a coil that looks like this:

- Sand one half of the ends of the coil. You should sand off only the insulation on the top part of the ends of the coil. Please check with your teacher before doing this to make sure you are sanding correctly. Most student built motors do not work because of improper sanding.

- Assemble a holder for your motor as shown on the next page. We will use a battery instead of the power supply shown here. Start with the battery disconnected.

- Spin your coil while holding it between index finger and thumb, one hand on each end of the coil, and adjust the ends of the wire so that it spins freely without wobbling.

- Place your coil in the paper clips and adjust the paper clips so that the coil is close to the magnet.

- Connect the paper clips to the battery. You may need to give your motor a slight spin to get it started.

- If your motor does not work, try adjusting the paper clips or the ends of the wire so that it spins freely and is close enough to the magnet.

- Try changing the position of the magnet, the voltage of the power supply, and the poles of the battery. Observe the effect on the speed and direction of the loop.

- Experiment with your motor and use your knowledge to find the answers to the following questions.

Questions:

- Why does the loop rotate?

- What modifications to your setup did you make to maximize the speed of the coil?

- Does your motor work in both directions? Why or why not? Give at least two ways to make the loop spin in the opposite direction.

- Why did you sand only one side of the ends of the loop?

- Come up with a unique name for your motor. What could it be used for?

Above and Beyond: Choose one of the following options to investigate:

- Get your motor to perform a task. Write a description of what you did and what happened. Include a diagram.

- Try to find a relationship between voltage and rate of spin. To do this, you need to measure both rates of spin and their associated voltages. Include a graph of rate of spin vs. voltage.

- Instead of using the magnets provided, make an electromagnet and use that on the bottom of the loop. Include a diagram, a description of what you did, and an assessment of your success at this task.

- How is this motor similar to an electric generator? What is a generator and how does one work? Try hooking your motor up to a multimeter (instead of the battery) and spinning the coil. Can you detect current? What is the most current you can produce?

- Write at least on well-written, complete paragraph about the history of electrical motors.