Series and Parallel Circuits Lab

In this lab, you will investigate a series and a parallel circuit in order to further your understanding of each type of circuit.

** Please use only the resistors provided for this lab so that you do not damage any of the equipment **

Part A – Series Circuit

1. Set up the series circuit as shown below.

2. Write down the color bands for each resistor in the data table. Find the values for each resistor using the color code chart. Check each resistor’s resistance using the Multimeter.

3. Connect the circuit and take your reading from the ammeter (or galvanometer). Record this in the data table.

4. Use the Multimeter to find the voltage drop across each resistor as well as across the whole circuit. Record these in the data table.

5. Disconnect the circuit quickly! Please do not miss this step.

Data Table

| Resistor # | First color | Second Color | Multiplier | Tolerance | Resistance | Voltage drop | Current |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 |  |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |  |
| Total for Circuit |  |  |  |  |  |  |  |

6. Calculate a theoretical voltage drop for each resistor, using what we learned about Ohm’s Law and series circuits in class. Compare this to the actual voltage drops (experimental) to compute a percent error. Record these in the results table below.

Results Table

|  | R1 | R2 | R3 | R4 |
| --- | --- | --- | --- | --- |
| Theoretical Voltage drop |  |  |  |  |
| Actual Voltage Drop |  |  |  |  |
| Percent Error |  |  |  |  |

Part B – Parallel Circuit

1. Set up the parallel circuit as shown below.

2. Write down the color bands for each resistor in the data table. Find the values for each resistor using the color code chart. Check each resistor’s resistance using the Multimeter.

3. Connect the circuit and take your reading from the ammeter (or galvanometer). Record this in the data table. Move the Ammeter to the next branch, and take your reading there. Continue until you have a reading for each resistor.

4. Use the Multimeter to find the voltage drop across the whole circuit.

5. Record the currents and voltage in the data table.

6. Disconnect the circuit quickly! Please do not miss this step.

Data Table

| Resistor # | First color | Second Color | Multiplier | Tolerance Band | Resistance | Voltage drop | Current |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 |  |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |  |
| Total for Circuit |  |  |  |  |  |  |  |

6. Calculate a theoretical current for each resistor, using what we learned about Ohm’s Law and parallel circuits in class. Compare this to the actual currents (experimental) to compute a percent error. Record these in the results table below.

Results Table

|  | R1 | R2 | R3 | R4 |
| --- | --- | --- | --- | --- |
| Theoretical Current |  |  |  |  |
| Actual Current |  |  |  |  |
| Percent Error |  |  |  |  |

Questions

- Why should you check the resistance with the Multimeter? Which method (color bands or Multimeter) do you think is more accurate? More reliable?

- What errors are present in this lab (please do not say human error!)?

- How could you make this lab better?

- Which setup best represents the electrical system in your house, parallel or series?

- Give 3 examples of series circuits in your everyday experience.

Group Reports are due.

For a 3 – Fill out tables, answer questions correctly, and hand in with everyone’s name on it.

For a 4 – Typed, full lab report format.

# Text boxes

Ammeter

Leave this connection until ready to take readings

2 batteries

R4

Ammeter

R4

R3

R2

R1

2 batteries

R3

Leave this connection until ready to take readings

R2

R1